## Slide 1: Digitizing measured section using StratCoreProcessor.m in Matlab R2014b (other versions not tested)
Sarah Southern
Lisa Stright

## Slide 2: Introduction
Slides cover the following:
File and folder naming.
Preparing a section in Illustrator.
Loading the digitizer.
Loading and setting up a section.
Adding bed top points.
Adding profile points.
Adding covered or missing intervals.
Saving and reloading work.
Accuracy.
QC digitization.
Editing points.

## Slide 3: Introduction
Practice the steps in the following slides on a small portion of a section before digitizing it in full.
Things will go wrong! It is easy to make errors and the digitizer has certain bugs that can result in merging or corruption of the different variables that you in put.
It is also important to check that the export to work space and mat file functions are working.

## Slide 4: Naming files & folders
For files that are used and saved, as well as the folders that they are stored in, avoid the following:
  Spaces
  Special characters (i.e. parentheses, commas, etc.)
  Numbers at the start of the file name
This commonly prevents use of the export matfile function required to save work in the digitizer.

## Slide 5: Prepare your section
Grain-size scale
Ensure the grain-size scale covers the full grain size range of your section (i.e. don’t stop at coarse sand if you have granules and pebbles).
The full scale is required to set up the horizontal scale in the digitizer.
It is easier to add a broad grain size scale to all logs rather than checking individual logs for their coarsest grain size.
Note that the digitizer only goes up to pebble grade.
  .

## Slide 6: Export the section as a .tiff file
Features
Keep it simple. Have the grain size profile, bed boundaries, color (sand vs. shale) and sedimentary structures.
Don’t include the original field scan – it’ll make it harder to resolve closely spaced and/or thin beds and features.
Consider reducing the stroke thickness of lines to improve accuracy.
Color
When exporting the .tiff file select the RGB color mode, not CMYK.

## Slide 7: Load the digitizer
Open Matlab
Navigate to the folder containing the CoreProcessing_v1.m file so that it appears in the current folder window.
Matlab main window:
Matlab main window:
Navigate to
directory
Workspace
window
Current
folder
window
Command window

## Slide 8: Load the digitizer
Double click CoreProcessing_v1.m in the current folder window (this loads the editor window and the script for the digitizer).
On the editor tab – click run to launch the digitizer window.
Editor window
Current
folder
window

## Slide 9: Load the digitizer
Expand the digitizer window to fit your screen or you will run into issues when using the zoom tool later.
Digitizer
window

## Slide 10: Load the section
Using Load  image – locate and select the section tiff file.

## Slide 11: Load the section
Add information (name, unit, environment of deposition, stratigraphic section) into Core ID and Core Loc – avoid using spaces or special characters.
Insert 0 if no location information is known.

## Slide 12: Zoom & pan tools
Right click when using the zoom or pan tool to access options.
Unconstrained zoom & pan – zoom in and out or move around the image in various directions.
Vertical zoom & pan – scroll up and down through the column with the mouse button.
Horizontal zoom & pan – scroll left and right with the mouse button.

## Slide 13: Set the vertical scale
Select zoom on the tool bar and zoom in on the top of your section.
Turn off zoom.
Turn on the set vertical scale radio button and place a point at the very top of the section
Enter the measurement at the top of the section into the “top” box (24 for 24m) - check your units match that stated in the Core ID section.
Reselect zoom
Right click the graphic log and select reset to original view.
Zoom in on the base of your section then deselect zoom.
Place a point at the very base of the section and insert the value in the “bottom” box.
Turn off set vertical scale radio.

## Slide 14: Set the grain size scale
Zoom in on the grain size scale, turn off zoom.
Turn on the grain size radio.
Place points on the top of the finest grain size category (e.g. clay @ 0.004 mm) and the top of the coarsest grain size category (e.g. granule @ 4.00 mm) only and set the corresponding grain sizes in the drop down menus beneath the grain size radio button.
Turn off the grain size radio button
Edited by L. Pettinga - June 2018

## Slide 15: Warning
Avoid having more than one radio button on at a time (see below)– doing so frequently merges different data types and Matlab does not warn you when this has occurred.

## Slide 16: Bed top points
Check that other radio buttons are turned off.
Turn on the log profile radio.
Activate the “bed top” digitize box (not the visible check box) so that it turns blue – this is now your active interpretation.

## Slide 17: Bed top points
Zoom in on the section so you can accurately place points at the following:
  The very base of of the section (0m).
  The top of all mudstones.
  The top of individual sedimentation units – don’t forget amalgamation surfaces.
Store points by clicking update active interp.
Note – turning off the log profile radio button before updating active interp will clear your points without saving them.

## Slide 18: Bed top points
Test if your points were stored:
Refresh the graphic log window by turning the log profile radio off and on again.
Check the visible box next to bed tops.
If stored, bed top points will appear as red dots.

## Slide 19: Bed profile points
To capture the grain size profile:
Turn off all radio buttons then turn on the log profile radio and click the bed profile digitize box.
Place a point at the base of all beds. For graded beds place enough points to capture the grain size profile.
Placing bed base points beneath the bed top point of the underlying bed will generate a false bed in the dataset.
Store points by clicking update interp.

## Slide 20: Bed profile points
Warning – Bed profile points often merge with bed top points the first time that they are stored.
After storing, refresh the graphic log (radio off an on log profile) and check the visible box for bed profile points.
If bed profile points are present at the top of the bed these data types have merged.
Check the bed profile digitize box, right click point and select delete all. Add add a new bed profile point and update active interp.

## Slide 21: Bed profile points
Bed top points can be made visible to guide placement of bed profile points:
Set bed tops to visible - these will show as red dots on the graphic log. Do not select the bed top digitize box – if you do radio off and on the log profile button.
Select the bed profile digitize box– these will show as blue dots indicating that these are the active interpretation.
Add bed profile points.
Before updating active interp. Turn off the bed top visible check box, reselect the bed profile digitize box and then click update active interp.
Notes: At the very base of the section (0m) this influences how Matlab reproduces the graphic log used to QC the section.
At the top of all shale beds
At the top of all sand beds – if sand beds are amalgamated just put at point on the amalgamation surface.

## Slide 22: Insert covered intervals
Place a bed top point at the top of the covered interval (blue arrow) and update active interp.
Deselect the log profile radio button and active the Shell radio button.
Select the No Recovery box (turns blue) and place a point somewhere in the covered interval (black arrow).
Update active interp.

## Slide 23: Saving
Before saving:
Make sure all radio buttons are turned off.
Check that used files, and the folders they are located in, do not have special characters or spaces in their name.
Make sure data has been input for the following:
  Core ID and location info.
  Vertical scale.
  Grain size scale.
  Some points for both bed tops and bed profiles.

## Slide 24: Saving
Export to workspace
  This updates the data in the workspace window of the main Matlab window.
Export to matfile
  Save as sectionname.mat (no special characters or spaces) in the same folder as the CoreProcessing_v1.m file or a sub-folder within this folder.
Periodically save different versions
  sectionname_v1.mat, sectionname__v2.mat, etc……..
  Things can go wrong so its good to keep back ups along the way.

## Slide 25: Saving
To save work as quickly as possible:
Enter Core ID and location info.
Set the Vertical scale.
Set Grain size scale.
Place a bed top point at the very base of the section and the top of the first sedimentation unit. Update active interp and radio off log profile.
Place a bed profile point somewhere along the grain size profile between these two points. Update active interp and radio off log profile.
Check that bed profile points have not merged with bed top points (see slides relating to bed profile points).
Export to workspace.
Export to matfile.

## Slide 26: Load saved files
Close the digitizer.
In the command window type clear, press return on the keypad, type clc and then press return again to clear the workspace.
Run CoreProcessing_v1.m to open the digitizer window and load the tiff file (see previous slides)
Reselect load, select points and select the saved .mat file
  Does turning on the vertical scale or grain size scale reload your points? Do bed top points and bed profile points occur in the correct place and are they separate from one another?
  Remember to not turn more than one radio button on at the same time and to turn the log profile radio off and on between checking different types of points.

## Slide 27: Accuracy
10cm
The digitizer resolution is good - sub cm scale resolution is possible at high zoom levels.
The limiting factor is the line thickness of our sections. The resolution is still around 2cm with the typical scale that we log at.
Reproduced log

## Slide 28: Accuracy
Note the curvature at the base of beds in drawn sections.
Unless your bed is inversely graded, make sure the bed profile point at the base accurately captures the grain size.
Notes: At the very base of the section (0m) this influences how Matlab reproduces the graphic log used to QC the section.
At the top of all shale beds
At the top of all sand beds – if sand beds are amalgamated just put at point on the amalgamation surface.

## Slide 29: Accuracy
Accurately distinguishing amalgamated and non-amalgamated beds
When the siltstones between sand beds are very thin they may not be drawn on the graphic log due to the scale at which we log. The sandstone beds appear amalgamated when they are not. This will likely only be an issue when digitizing sections drawn by other people as you will be aware of you own data.
An over estimation of the amalgamation index could influence a number of factors. Are you using it to define the position within a channel or lobe, to consider fluid flow, to consider temporal variations in stratigraphy etc... Even if you are not interested in amalgamation index, someone else might be in the future so it is important to capture this information.
Thin silts
not
shown

## Slide 30: Accuracy
Accurately distinguishing amalgamated and non-amalgamated beds
When you see relatively thin beds with no siltstone partings – check the original field descriptions to see if siltstones are present.
Using a high zoom, try and capture these siltstones by placing bed tops for siltstones (black arrow) on the boundary between beds just above the bed top point of the underlying sandstone bed (blue arrow).
Caution - If the bed top point for the silt is placed beneath the bed top point for the sand an extra pseudo-bed will be generated in your data.
Tip - Use the horizontal axis as a guide to show you which point is highest (bottom image). This is also useful if you have very thin beds.
Top silt
Top sand

## Slide 31: QC the digitization
Locate the Zstratplot.m file in the current folder window.
In the command window type Zstratplot(C) and press return.
A figure window with your digitized log will appear.
Use the zoom and pan tool compare with the original section
  Check the vertical and grain size scales are accurate
  Check the appropriate number of beds has been created
  Check that bed profiles are realistic.

## Slide 32: QC the digitization
A bed top point was not placed at the very base of the section
A coarser grained bed profile point has been placed above a finer grained bed profile point. Unless you have inverse grading this is wrong.
Common errors

## Slide 33: QC the digitization
A bed top point was missing.
Common errors

## Slide 34: Editing points
Return to the digitizer.
Turn on the appropriate radio button and select the digitize box for the property you want to edit.
You can delete (right click), move or add points. You can delete a single point or all points for the property that you are digitizing.
Remember to update active interp before starting to edit a different property otherwise the changes will not be stored.
It is also a good idea to save at this point (export to the workspace and export to a matfile) before editing other another property.

## Slide 35: Sedimentary features
Facies and sedimentary features are not reproduced by running Zstratplot.m
I’d suggest holding off on digitizing sedimentary features and facies in case the way we store this information in the Matlab structure changes if we have to develop our own scripts to analyze these.